## Slide 1: Projective Geometry and Camera Models
Computer Vision
Jia-Bin Huang, Virginia Tech
Many slides from S. Seitz and D. Hoiem

## Slide 2: Administrative stuffs
HWs
  HW 1 is back
  HW 2 due 11:59 PM on Oct 3rd.
  Frequently asked questions for HW 2
  HW 3 should be out by the end of this week
Think about your final projects
  work in groups of 2-4
  should evince independent effort to learn about a new topic, try something new, or apply to an application of interest
  Proposals will be due Oct 27

## Slide 3: Top edge methods – average F-score
Subhashree (0.673)
  Canny for different channels with oriented filters
Shruti Phadke (0.66)
  Simple Gradient, colour channel splitting
Ben Zhao (0.658)
  Oriented Elongated Gaussian
Excellent HW 1 report:
Badour AlBahar

## Slide 4: Review: Interpreting Intensity
Light and color
  What an image records
Filtering in spatial domain
  Filtering = weighted sum of neighboring pixels
  Smoothing, sharpening, measuring texture
Filtering in frequency domain
  Filtering = change frequency of the input image
  Denoising, sampling, image compression
Image pyramid and template matching
  Filtering = a way to find a template
  Image pyramids for coarse-to-fine search and multi-scale detection
Edge detection
  Canny edge = smooth -> derivative -> thin -> threshold -> link
  Finding straight lines, binary image analysis

## Slide 5: Review: Correspondence and Alignment
Interest points
  Find distinct and repeatable points in images
  Harris-> corners, DoG -> blobs
  SIFT -> feature descriptor
Feature tracking and optical flow
  Find motion of a keypoint/pixel over time
  Lucas-Kanade:
    brightness consistency, small motion, spatial coherence
  Handle large motion:
    iterative update + pyramid search
Fitting and alignment
  find the transformation parameters that best align matched points
Object instance recognition
  Keypoint-based object instance recognition and search

## Slide 6: Perspective and 3D Geometry
Projective geometry and camera models
  What’s the mapping between image and world coordiantes?
Single view metrology and camera calibration
  How can we measure the size of 3D objects in an image?
  How can we estimate the camera parameters?
Photo stitching
  What’s the mapping from two images taken without camera translation?
Epipolar Geometry and Stereo Vision
  What’s the mapping from two images taken with camera translation?
Structure from motion
  How can we recover 3D points from multiple images?

## Slide 7: Next two classes: Single-view Geometry
How tall is this woman?
Which ball is closer?
How high is the camera?
What is the camera rotation?
What is the focal length of the camera?

## Slide 8: Today’s class Mapping between image and world coordinates
Pinhole camera model
Projective geometry
  Vanishing points and lines
Projection matrix
Vanishing
point
Vanishing
line
Vanishing
point
Vertical vanishing
point
(at infinity)

## Slide 9: Image formation
Let’s design a camera
  Idea 1: put a piece of film in front of an object
  Do we get a reasonable image?
Slide source: Seitz

## Slide 10: Pinhole camera
Idea 2: add a barrier to block off most of the rays
  This reduces blurring
  The opening known as the aperture
Slide source: Seitz
Notes: Q: How does this transform the image? A: It gets inverted

## Slide 11: Pinhole camera
Figure from Forsyth
f
f = focal length
c = center of the camera
c

## Slide 12: Camera obscura: the pre-camera
First idea: Mo-Ti, China (470BC to 390BC)
First built: Alhazen, Iraq/Egypt (965 to 1039AD)
Illustration of Camera Obscura
Freestanding camera obscura at UNC Chapel Hill
Photo by Seth Ilys
Notes: Alhazen was born in Basra, moved to Egypt. Proposed to the king to control the Nile with a dam. Realized he couldn’t do it and feigned madness until the king died. During that time, he wrote the book of optics.

## Slide 13: Camera Obscura used for Tracing
Lens Based Camera Obscura, 1568

## Slide 14: First Photograph
Oldest surviving photograph
  Took 8 hours on pewter plate
Joseph Niepce, 1826
Photograph of the first photograph
Stored at UT Austin
Niepce later teamed up with Daguerre, who eventually created Daguerrotypes

## Slide 15: Dimensionality Reduction Machine (3D to 2D)
Figures © Stephen E. Palmer, 2002
3D world
2D image

## Slide 16: Projection can be tricky…
Slide source: Seitz

## Slide 17: Projection can be tricky…
Slide source: Seitz
Making of 3D sidewalk art: http://www.youtube.com/watch?v=3SNYtd0Ayt0

## Slide 18
What is lost?
Length
Which is closer?
Who is taller?
Projective Geometry

## Slide 19: Length is not preserved
Figure by David Forsyth
B’
C’
A’

## Slide 20: Projective Geometry
What is lost?
Length
Angles
Perpendicular?
Parallel?

## Slide 21: Projective Geometry
What is preserved?
Straight lines are still straight

## Slide 22: Vanishing points and lines
Parallel lines in the world intersect in the image at a “vanishing point”
Notes: Go to board, sketch out various properties of vanishing points/lines

## Slide 23: Vanishing points

## Slide 24: Vanishing points and lines
o
Vanishing Point
o
Vanishing Point
Vanishing Line
The projections of parallel 3D lines intersect at a vanishing point
The projection of parallel 3D planes intersect at a vanishing line
If a set of parallel 3D lines are also parallel to a particular plane, their vanishing point will lie on the vanishing line of the plane
Not all lines that intersect are parallel
Vanishing point <-> 3D direction of a line
Vanishing line <-> 3D orientation of a surface
Notes: Go to board, sketch out various properties of vanishing points/lines
Parallel lines intersect at a point
The intersection of red lines and blue lines form a parallelogram
Sets of parallel lines on the same plane form a vanishing line
Sets of parallel planes form a vanishing line
Not all lines that intersect are parallel

## Slide 25: Vanishing points and lines
Vanishing
point
Vanishing
line
Vanishing
point
Vertical vanishing
point
(at infinity)
Slide from Efros, Photo from Criminisi

## Slide 26: Vanishing points and lines
Photo from online Tate collection
Notes: Where are the vanishing points? Do buildings on left and buildings on right have the same vanishing line? Which way is the camera tilted?

## Slide 27: Note on estimating vanishing points
Use multiple lines for better accuracy
… but lines will not intersect at exactly the same point in practice
One solution: take mean of intersecting pairs
… bad idea!
Instead, minimize angular differences
Notes: Go to board, sketch out various properties of vanishing points/lines

## Slide 28: Vanishing objects

## Slide 29: Projection: world coordinatesimage coordinates
Camera Center (tx, ty, tz)
.
.
.
f
Z
Y
.
Optical Center (u0, v0)
v
u
X

## Slide 30: Homogeneous coordinates
Converting to homogeneous coordinates
homogeneous image
coordinates
homogeneous scene
coordinates
Converting from homogeneous coordinates
Is this a linear transformation?
  no—division by z is nonlinear
Notes: Append coordinate with value 1; proportional coordinate system

## Slide 31: Homogeneous coordinates
Invariant to scaling
Point in Cartesian is ray in Homogeneous
Homogeneous Coordinates
Cartesian Coordinates
Notes: Q: Suppose we have a point in Cartesian coordinates. What is that in homogeneous coordinates? A: a ray

## Slide 32: Basic geometry in homogeneous coordinates
Append 1 to pixel coordinate to get homogeneous coordinate
Line equation:
Line given by cross product of two points
Intersection of two lines given by cross product of the lines
Three points lies on the same line
Three lines intersect at the same point

## Slide 33: Another problem solved by homogeneous coordinates
Intersection of parallel lines
  Cartesian: (Inf, Inf)
  Homogeneous: (1, 1, 0)
  Cartesian: (Inf, Inf)
Homogeneous: (1, 2, 0)
Notes: Parallel lines intersect at different infinities

## Slide 34: Interlude: where can this be useful?

## Slide 35: Applications
Object Recognition (CVPR 2006)

## Slide 36: Applications
Single-view reconstruction (SIGGRAPH 2005)

## Slide 37: Applications
Getting spatial layout in indoor scenes (ICCV 2009)

## Slide 38: Applications
Inserting synthetic objects into images: http://vimeo.com/28962540

## Slide 39: Applications
Creating detailed and complete 3D scene models from a single view

## Slide 40: Perspective Projection Matrix
divide by the third coordinate
Projection is a matrix multiplication using homogeneous coordinates
In practice: lots of coordinate transformations…
World to camera coord. trans. matrix (4x4)
Perspective projection matrix (3x4)
Camera to pixel coord. trans. matrix (3x3)
=
2D
point (3x1)
3D point (4x1)

## Slide 41
Slide Credit: Saverese
Projection matrix
x: Image Coordinates: (u,v,1)
K: Intrinsic Matrix (3x3)
R: Rotation (3x3)
t: Translation (3x1)
X: World Coordinates: (X,Y,Z,1)
Ow
iw
kw
jw
R,T
Notes: We can use homogeneous coordinates to write camera matrix in linear form.

## Slide 42
K
Slide Credit: Saverese
Projection matrix
Intrinsic Assumptions
Unit aspect ratio
Optical center at (0,0)
No skew
Extrinsic Assumptions
No rotation
Camera at (0,0,0)
Notes: Work through equations for u and v on board

## Slide 43: Remove assumption: known optical center
Intrinsic Assumptions
Unit aspect ratio
No skew
Extrinsic Assumptions
No rotation
Camera at (0,0,0)

## Slide 44: Remove assumption: square pixels
Intrinsic Assumptions
No skew
Extrinsic Assumptions
No rotation
Camera at (0,0,0)

## Slide 45: Remove assumption: non-skewed pixels
Intrinsic Assumptions
Extrinsic Assumptions
No rotation
Camera at (0,0,0)
Note: different books use different notation for parameters

## Slide 46: Oriented and Translated Camera
Ow
iw
kw
jw
t
R

## Slide 47: Allow camera translation
Intrinsic Assumptions
Extrinsic Assumptions
No rotation

## Slide 48: 3D Rotation of Points
Rotation around the coordinate axes, counter-clockwise:
p
p’
g
y
z
Slide Credit: Saverese

## Slide 49: Allow camera rotation

## Slide 50: Degrees of freedom
5
6
Notes: How many known points are needed to estimate this?

## Slide 51: Vanishing Point = Projection from Infinity

## Slide 52: Scaled Orthographic Projection
Special case of perspective projection
  Object dimensions are small compared to distance to camera
  Also called “weak perspective”
Image
World
Slide by Steve Seitz

## Slide 53: Orthographic Projection - Examples

## Slide 54: Orthographic Projection - Examples

## Slide 55: Applications in object detection
Near field: object appearance changes as objects translate
Far field: object appearance doesn’t change as objects translate

## Slide 56: Beyond Pinholes: Radial Distortion
Common in wide-angle lenses or for special applications (e.g., security)
Creates non-linear terms in projection
Usually handled by through solving for non-linear terms and then correcting image
Image from Martin Habbecke
Corrected Barrel Distortion

## Slide 57: Things to remember
Vanishing points and vanishing lines
Pinhole camera model and camera projection matrix
Homogeneous coordinates
Vanishing
point
Vanishing
line
Vanishing
point
Vertical vanishing
point
(at infinity)

## Slide 58: Next class Applications of camera model and projective geometry
Recovering the camera intrinsic and extrinsic parameters from an image
Measuring size in the world
Projecting from one plane to another