## Slide 1: Epipolar Geometry and Stereo Vision
Computer Vision
Jia-Bin Huang, Virginia Tech
Many slides from S. Seitz and D. Hoiem

## Slide 2: Last class: Image Stitching
Two images with rotation/zoom but no translation
f
f'
.
x
x'
X

## Slide 3: This class: Two-View Geometry
Epipolar geometry
  Relates cameras from two positions
Stereo depth estimation
  Recover depth from two images

## Slide 4: Depth from Stereo
Goal: recover depth by finding image coordinate x’ that corresponds to x
f
x
x’
Baseline B
z
C
C’
X
f
X
x
x'

## Slide 5: Depth from Stereo
Goal: recover depth by finding image coordinate x’ that corresponds to x
Sub-Problems
  Calibration: How do we recover the relation of the cameras (if not already known)?
  Correspondence: How do we search for the matching point x’?
X
x
x'

## Slide 6: Correspondence Problem
We have two images taken from cameras with different intrinsic and extrinsic parameters
How do we match a point in the first image to a point in the second? How can we constrain our search?
x
?

## Slide 7: Key idea: Epipolar constraint

## Slide 8: Key idea: Epipolar constraint
Potential matches for x have to lie on the corresponding line l’.
Potential matches for x’ have to lie on the corresponding line l.
x
x’
X
x’
X
x’
X

## Slide 9: Epipolar geometry: notation
Epipolar Plane – plane containing baseline (1D family)
Epipoles
= intersections of baseline with image planes
= projections of the other camera center
Baseline – line connecting the two camera centers
X
x
x’

## Slide 10: Epipolar geometry: notation
Epipolar Lines - intersections of epipolar plane with image planes (always come in corresponding pairs)
X
x
x’
Epipolar Plane – plane containing baseline (1D family)
Epipoles
= intersections of baseline with image planes
= projections of the other camera center
Baseline – line connecting the two camera centers

## Slide 11: Example: Converging cameras

## Slide 12: Example: Motion parallel to image plane

## Slide 13: Example: Forward motion
What would the epipolar lines look like if the camera moves directly forward?

## Slide 14: Example: Forward motion
e
e’
Epipole has same coordinates in both images.
Points move along lines radiating from e: “Focus of expansion”

## Slide 15: Epipolar constraint: Calibrated case
X
x
x’
Given the intrinsic parameters of the cameras:
  Convert to normalized coordinates by pre-multiplying all points with the inverse of the calibration matrix; set first camera’s coordinate system to world coordinates
Homogeneous 2d point (3D ray towards X)
2D pixel coordinate (homogeneous)
3D scene point
3D scene point in 2nd camera’s 3D coordinates

## Slide 16: Epipolar constraint: Calibrated case
X
x
x’
Given the intrinsic parameters of the cameras:
  Convert to normalized coordinates by pre-multiplying all points with the inverse of the calibration matrix; set first camera’s coordinate system to world coordinates
  Define some R and t that relate X to X’ as below
for some scale factor

## Slide 17: Epipolar constraint: Calibrated case
x
x’
X
(because and are co-planar)
Notes: X’ is X in the second camera’s coordinate system
We can identify the non-homogeneous 3D vectors X and X’ with the homogeneous coordinate vectors x and x’ of the projections of the two points into the two respective images

## Slide 18: Essential matrix
Essential Matrix
(Longuet-Higgins, 1981)
X
x
x’
Notes: [t]x is the skew symmetric matrix of t

## Slide 19: Properties of the Essential matrix
X
E x’ is the epipolar line associated with x’ (l = E x’)
ETx is the epipolar line associated with x (l’ = ETx)
E e’ = 0 and ETe = 0
E is singular (rank two)
E has five degrees of freedom
  (3 for R, 2 for t because it’s up to a scale)
Drop ^ below to simplify notation
x
x’
Skew-symmetric matrix

## Slide 20: Epipolar constraint: Uncalibrated case
If we don’t know K and K’, then we can write the epipolar constraint in terms of unknown normalized coordinates:
X
x
x’

## Slide 21: The Fundamental Matrix
Fundamental Matrix
(Faugeras and Luong, 1992)
Without knowing K and K’, we can define a similar relation using unknown normalized coordinates

## Slide 22: Properties of the Fundamental matrix
F x’ is the epipolar line associated with x’ (l = F x’)
FTx is the epipolar line associated with x (l’ = FTx)
F e’ = 0 and FTe = 0
F is singular (rank two): det(F)=0
F has seven degrees of freedom: 9 entries but defined up to scale, det(F)=0
X
x
x’

## Slide 23: Estimating the Fundamental Matrix
8-point algorithm
  Least squares solution using SVD on equations from 8 pairs of correspondences
  Enforce det(F)=0 constraint using SVD on F
7-point algorithm
  Use least squares to solve for null space (two vectors) using SVD and 7 pairs of correspondences
  Solve for linear combination of null space vectors that satisfies det(F)=0
Minimize reprojection error
  Non-linear least squares
Note: estimation of F (or E) is degenerate for a planar scene.

## Slide 24: 8-point algorithm
Solve a system of homogeneous linear equations
  Write down the system of equations
=0

## Slide 25: 8-point algorithm
Solve a system of homogeneous linear equations
  Write down the system of equations
  Solve f from Af=0 using SVD
Matlab:
[U, S, V] = svd(A);
f = V(:, end);
F = reshape(f, [3 3])’;

## Slide 26: Need to enforce singularity constraint

## Slide 27: 8-point algorithm
Solve a system of homogeneous linear equations
  Write down the system of equations
  Solve f from Af=0 using SVD
Resolve det(F) = 0 constraint using SVD
Matlab:
[U, S, V] = svd(A);
f = V(:, end);
F = reshape(f, [3 3])’;
Matlab:
[U, S, V] = svd(F);
S(3,3) = 0;
F = U*S*V’;

## Slide 28: 8-point algorithm
Solve a system of homogeneous linear equations
  Write down the system of equations
  Solve f from Af=0 using SVD
Resolve det(F) = 0 constraint by SVD
Notes:
Use RANSAC to deal with outliers (sample 8 points)
  How to test for outliers?
Solve in normalized coordinates
  mean=0
  standard deviation ~= (1,1,1)
  just like with estimating the homography for stitching
Notes: Test for outliers by computing distance from epipolar line to corresponding point (NOT by taking square of xTFx’)

## Slide 29
Homography (No Translation)
Fundamental Matrix (Translation)
Correspondence Relation
Normalize image coordinates
RANSAC with 8 points
  Initial solution via SVD
  Enforce by SVD
De-normalize:
Correspondence Relation
Normalize image coordinates
RANSAC with 4 points
  Solution via SVD
De-normalize:
Comparison of homography estimation and the 8-point algorithm
Assume we have matched points x x’ with outliers

## Slide 30: 7-point algorithm
Faster (need fewer points) and could be more robust (fewer points), but also need to check for degenerate cases

## Slide 31: “Gold standard” algorithm
Use 8-point algorithm to get initial value of F
Use F to solve for P and P’ (discussed later)
Jointly solve for 3d points X and F that minimize the squared re-projection error
X
x
x'
See Algorithm 11.2 and Algorithm 11.3 in HZ (pages 284-285) for details

## Slide 32: Comparison of estimation algorithms
 | 8-point | Normalized 8-point | Nonlinear least squares
Av. Dist. 1 | 2.33 pixels | 0.92 pixel | 0.86 pixel
Av. Dist. 2 | 2.18 pixels | 0.85 pixel | 0.80 pixel

## Slide 33: We can get projection matrices P and P’ up to a projective ambiguity
Code:
function P = vgg_P_from_F(F)
[U,S,V] = svd(F);
e = U(:,3);
P = [-vgg_contreps(e)*F e];
See HZ p. 255-256
K’*translation
K’*rotation
If we know the intrinsic matrices (K and K’), we can resolve the ambiguity

## Slide 34: From epipolar geometry to camera calibration
Estimating the fundamental matrix is known as “weak calibration”
If we know the calibration matrices of the two cameras, we can estimate the essential matrix: E = KTFK’
The essential matrix gives us the relative rotation and translation between the cameras, or their extrinsic parameters

## Slide 35: Let’s recap…
Fundamental matrix song

## Slide 36: Moving on to stereo…
Fuse a calibrated binocular stereo pair to produce a depth image
image 1
image 2
Dense depth map
Many of these slides adapted from Steve Seitz and Lana Lazebnik

## Slide 37: Basic stereo matching algorithm
For each pixel in the first image
  Find corresponding epipolar line in the right image
  Search along epipolar line and pick the best match
  Triangulate the matches to get depth information
Simplest case: epipolar lines are scanlines
  When does this happen?

## Slide 38: Simplest Case: Parallel images
Image planes of cameras are parallel to each other and to the baseline
Camera centers are at same height
Focal lengths are the same

## Slide 39: Simplest Case: Parallel images
Image planes of cameras are parallel to each other and to the baseline
Camera centers are at same height
Focal lengths are the same
Then, epipolar lines fall along the horizontal scan lines of the images

## Slide 40: Simplest Case: Parallel images
Epipolar constraint:
R = I t = (T, 0, 0)
The y-coordinates of corresponding points are the same
t
x
x’

## Slide 41: Depth from disparity
f
x’
Baseline B
z
O
O’
X
f
Disparity is inversely proportional to depth.
x

## Slide 42: Stereo image rectification

## Slide 43: Stereo image rectification
Reproject image planes onto a common plane parallel to the line between camera centers
Pixel motion is horizontal after this transformation
Two homographies (3x3 transform), one for each input image reprojection
C. Loop and Z. Zhang. Computing Rectifying Homographies for Stereo Vision. IEEE Conf. Computer Vision and Pattern Recognition, 1999.

## Slide 44: Rectification example

## Slide 45: Basic stereo matching algorithm
If necessary, rectify the two stereo images to transform epipolar lines into scanlines
For each pixel x in the first image
  Find corresponding epipolar scanline in the right image
  Search the scanline and pick the best match x’
  Compute disparity x-x’ and set depth(x) = fB/(x-x’)

## Slide 46: Correspondence search
Matching cost
disparity
Left
Right
scanline
Slide a window along the right scanline and compare contents of that window with the reference window in the left image
Matching cost: SSD or normalized correlation

## Slide 47: Correspondence search
Left
Right
scanline
SSD

## Slide 48: Correspondence search
Left
Right
scanline
Norm. corr

## Slide 49: Effect of window size
W = 3
W = 20
Smaller window
  + More detail
  More noise
Larger window
  + Smoother disparity maps
  Less detail
  Fails near boundaries
Notes: smaller window: more detail, more noise
bigger window: less noise, more detail

## Slide 50: Failures of correspondence search
Textureless surfaces
Occlusions, repetition
Non-Lambertian surfaces, specularities

## Slide 51: Results with window search
Window-based matching
Ground truth
Data

## Slide 52: How can we improve window-based matching?
So far, matches are independent for each point
What constraints or priors can we add?

## Slide 53: Stereo constraints/priors
Uniqueness
  For any point in one image, there should be at most one matching point in the other image

## Slide 54: Stereo constraints/priors
Uniqueness
  For any point in one image, there should be at most one matching point in the other image
Ordering
  Corresponding points should be in the same order in both views

## Slide 55: Stereo constraints/priors
Uniqueness
  For any point in one image, there should be at most one matching point in the other image
Ordering
  Corresponding points should be in the same order in both views
Ordering constraint doesn’t hold

## Slide 56: Priors and constraints
Uniqueness
  For any point in one image, there should be at most one matching point in the other image
Ordering
  Corresponding points should be in the same order in both views
Smoothness
  We expect disparity values to change slowly (for the most part)

## Slide 57: Stereo matching as energy minimization
I1
I2
D
Energy functions of this form can be minimized using graph cuts
  Y. Boykov, O. Veksler, and R. Zabih, Fast Approximate Energy Minimization via Graph Cuts, PAMI 2001
W1(i )
W2(i+D(i ))
D(i )

## Slide 58: Many of these constraints can be encoded in an energy function and solved using graph cuts
Graph cuts
Ground truth
    For the latest and greatest: http://www.middlebury.edu/stereo/
  Y. Boykov, O. Veksler, and R. Zabih, Fast Approximate Energy Minimization via Graph Cuts, PAMI 2001
Before

## Slide 59: Things to remember
Epipolar geometry
  Epipoles are intersection of baseline with image planes
  Matching point in second image is on a line passing through its epipole
  Fundamental matrix maps from a point in one image to a line (its epipolar line) in the other
  Can solve for F given corresponding points (e.g., interest points)
  Can recover canonical camera matrices from F (with projective ambiguity)
Stereo depth estimation
  Estimate disparity by finding corresponding points along scanlines
  Depth is inverse to disparity

## Slide 60: Next class: structure from motion